### Test 050-04-04 New After Busy
Determine proper use of the BUSY response code 0x79 and the proper processing of the BUSY response in the case where the BUSY response is met with a new command
##### PD
If the PD is unable to accept the command for processing due to temporary unavailability of a resource required to process the command, then the PD may send the osdp_BUSY reply as defined in subclause 7.19. In this case the BUSY response if met with a new command.
##### ACU
ACU may process the osdp_BUSY response and determine the need to process a new command.
#### Purpose
Used by PD to let ACU know that it is still processing a command and allows the ACU to determine next step, such as a new command, after its latest command received an osdp_BUSY.
#### Criteria

Basic OSDP (PD)	Required
Basic OSDP (ACU)	Optional
Secure Channel (PD)	Required
Secure Channel (ACU)	Optional
BIO Match (PD)	Required
BIO Match (ACU)	Optional
BIO Read (PD)	Required
BIO Read (ACU)	Optional
Extended Packet Mode (PD)	Required
Extended Packet Mode (ACU)	Optional
Extended Read/Write (PD)	Required
Extended Read/Write (ACU)	Optional

#### Test action
##### PD Test
The PD is in a state where it issues an osdp_BUSY reply, the ACU sends a new command, and the PD maintains communication with the ACU until it can complete the process underway and continue with processing commands.
##### ACU Test
#### When the ACU receives the osdp_BUSY reply, it may, at its discretion, choose to the same command as it would if the command delivery timed out. If, on the other hand, the ACU elects to abandon the command that received the BUSY reply, the PD shall recognize this condition (new sequence number) and shall process the new command.
#### Development status
Available in libosdp-conformance 1.32-Build-2
#### Test Results
JSON tags
test	050-04-2
test-status	1 for pass, 0 for fail

#### Revision History
New as 2.4.2
Updated as 2.5.3