### Test 050-08-01 Message Synchronization
General procedure for a PD to pass message traffic and perform message synchronization.
##### PD
The PD MUST maintain synchronization as described in section 5.8. The nominal value of the inter-character timeout shall be 20 milliseconds. This parameter may need to be adjusted for special channel timing considerations.
##### ACU
The ACU MUST maintain synchronization as described in section 5.8. The nominal value of the inter-character timeout shall be 20 milliseconds. This parameter may need to be adjusted for special channel timing considerations.

#### Purpose
Used to maintain PD and ACU synchronization
#### Criteria

Basic OSDP (PD)	Required
Basic OSDP (ACU)	Required
Secure Channel (PD)	Required
Secure Channel (ACU)	Required
BIO Match (PD)	Required
BIO Match (ACU)	Required
BIO Read (PD)	Required
BIO Read (ACU)	Required
Extended Packet Mode (PD)	Required
Extended Packet Mode (ACU)	Required
Extended Read/Write (PD)	Required
Extended Read/Write (ACU)	Required

#### Test action
##### PD Test
Plug PD into RS-485 test jig and make sure it works. Requires choosing a speed at which to test. Assumes proper inter-character timing if the testing works.
Use a logic analyzer for further verification.
##### ACU Test
Plug ACU into RS-485 test jig and make sure it works. Requires choosing a speed at which to test. Assumes proper inter-character timing if the testing works.
Use a logic analyzer for further verification.

#### Development status
n/a

#### Test Results
JSON tags
test	n/a
test-status	n/a

#### Revision History
Updated as 2.4.2