OSPD Verified Test Descriptions
2.0.2-2

# Introduction
How to read this document
about the test naming

uses numbering from published 60839-11-5
# Test Descriptions
## Test Group 5 – Protocol
### Test 050-01-01 Physical Interface
Test Reference: 050-01-01 (rev.01)
Test Title: Physical Interface
Criteria: (required: basic) supports RS-485 2-wire
Test action: plug it in to RS-485 test jig and make sure it works. Requires choosing a speed at which to test.
Operator action:
1. confirm initial set-up.
2. confirm interview form complete.
3. set up at designated address/speed.
4. connect DUT
5. confirm at least 8 poll/ack sequences completed.
Recommended processing: n/a
### Test-draft 050-01-02 TCP Interface
t.b.d.
Criteria: (optional) support TCP as implemented in the reference implementation including "kick-not-poll" processing.
Recommended processing: n/a
### Test 050-02-01 Signalling
Test Reference: 050-02-01 (rev. 01)
Test Title: Signalling
Criteria: (required) supports at least one of the designated speeds.
Test action: confirm communications at designated speed. See interview form.
Operator action:
use speed from form
confirm testbed is running at that speed
connect DUT
confirm at least 8 poll/ack sequences completed
Recommended processing: n/a
### Test 050-03-01 Character Encoding
Test Reference: 050-03-01 (rev. 01)
Test Title: Character Encoding
Criteria: (required) support use of all possible 8 bit patterns.
Test action: Use OSDP trace to confirm character coverage.
Operator action:
Exercise DUT through full test set, collecting a trace
Confirm successful operation
Run trace analyzer
Report character coverage
Recommended processing: n/a
### Test 050-04-01 Channel Access
Test Reference: 050-04-01 (rev. 02)
Test Title: Channel Access
Criteria: (required) Confirm only one reply per command; presence of busy; later processing if busy.
Test action: Use OSDP trace to confirm presence of busy, one reply per command.
Operator action:
Set up DUT and run a selection of commands, collecting a trace
Run trace analyzer
Confirm analyzer does not report response anomalies.
Recommended processing: n/a
### Test-draft 050-04-02 Retry
tbd required
at test ACU by command drop a response and send the last command again. make sure the PD behaves correctly - no nak, processes the command again (?)
### Test-draft 050-05-01 Multibyte Encoding
tbd required
?? test from ACU to PD
?? test from PD to ACU
050-05-01,Multi-byte Data Encoding,lsb first unless otherwise noted; no padding.
### Test-draft 050-06-01 Packet Size Limits
tbd required
RUN PDCAP TEST FIRST AND VERIFY PDCAP RESPONSE INCLUDES MAX PACKET SIZE
try a text out at the 128 limit, make sure you get "bad command" not "bad command", then try an out-of-spec packet and make sure you get "bad packet" not "bad command". use pdcap to identify max size claimed to be accepted by PD.

also, send a truly max sized packet using LED commands to a different address and ensure the PD does not fail. fail is defined as reboot, stop accepting poll, etc.
### Test 050-07-01 Timing
Test Reference: 050-07-01 (rev. 00)
Test Title: Timing
Criteria: (required) Confirm command (poll) response time is under 200 milliseconds.
Test action: Use OSDP trace log analyzer to confirm timing.
Operator action:
Set up DUT in idle poll/ack configuration, collecting a trace
Run trace analyzer
Confirm analyzer does not report response time of 200ms exceeded.
Recommended processing: n/a
### Test 050-08-01 Message Synchronization
Test Reference: 050-08-01 (rev. 00)
Test Title: Message Synchronization
Criteria: (required) Passes message traffic (implied.)
Test action: plug it in to RS-485 test jig and make sure it works. Requires choosing a speed at which to test. Assumes proper inter-character timing if the testing works.
Operator action: plug it in.
Recommended processing: n/a; Use a logic analyzer for further verification.
### Test 050-09-01 Packet Format
050-09-01,Packet Format,follow table 1 packet format.
### Test 050-09-15 CRC
Test Reference: 050-09-15 (rev 00)
Test Title: Command/Response use of CRC
Description:
All commands and responses are expected to use CRC checks (not checksum.)
Purpose:
Confirm implementation uses compatible CRC calculation.
Criteria:
Required: ACU-Basic, PD-Basic
Test action:
Configure test stand for CRC operation and confirm DUT matches.
Operator action:
PD test: Confirm ACU uses CRC not checksum
ACU test: Confirm ACU sends and can receive CRC
Recommended processing:
Use CRC always, never use checksum (as it's legacy and not secure.)
Development status: Available in libosdp-conformance 1.01 Build 2)
Example use: t.b.d.

### Test 050-09-16 Bad CRC in Response
Test Reference: 050-09-16 (rev 00)
Test Title: Bad CRC in Response
Description:
Check to confirm ACU can detect a bad CRC in an OSDP response from a PD.
Purpose:
Confirm error check logic.
Criteria:
Required: ACU-Basic
Not required: PD (any)
Test action: Use test stand to cause a malformed response to be returned to an ACU DUT.
Operator action:
PD test: n/a
ACU test: via test stand activate conformance test 050-09-16
Recommended processing:
ACU has to at least not accept the packet. It may resend the last command if it wishes. ACU is recommended to be instrumented so telemetry reflects the condition has happened.
Development status: Not yet available in libosdp-conformance (as of 1.01 build 2)
Example use: t.b.d.

### Test 050-09-17 Bad CRC in Command
Test Reference: 050-09-17 (rev 00)
Test Title: Bad CRC in Command
Description:
Check to confirm PD can detect a bad CRC in an OSDP command from an ACU.
Purpose:
Confirm error check logic.
Criteria:
Required: PD-Basic
Not required: ACU (any)
Test action: Use test stand to cause a malformed command to be sent to a PD DUT.
Operator action:
PD test: via test stand activate conformance test 050-09-17
ACU test: n/a
Recommended processing:
PD must not accept the packet. PD is expected to send a NAK. PD is expected to be prepared to handle retransmission of the command. Sequence number must not advance. Secure channel session must not advance MAC (the frame was bad, no the secure channel 'stream'.)
Development status: Not yet available in libosdp-conformance (as of 1.01 build 2)
Example use: t.b.d.

### Other 050 tests
050-02-01,,
050-04-04,,
050-09-16,,
050-01-03,TLS,
050-02-02,"SIgnalling 19,200",
050-02-03,"Signalling 38,400",
050-02-04,"Signalling 115,200",
050-02-05,"Signalling 57,600",
050-02-06,"Signalling 230,400",
050-04-03,resend busy,
050-04-04,new after busy,

050-06-01,Packet Size Limits ACU to PD,accept at least 128 bytes total pdu size; accept max 1440 bytes total PDU size.
050-06-02,Packet Size Limits PD to ACU,

050-09-02,,process sequence 0
050-09-03,SOM - Start of Message,SOM starts each OSDP command and response
050-09-04,ADDR - Address,Address field indicates PD address 0x00-0x7e inclusive or special configuration address 0x7f
050-09-05,,"must not use 7f except for ID,PDID, CAP, PDCAP, COM, COMSET"
050-09-06,LEN - Length,Length field (2 bytes LSB MSB) indicates length of OSDP command and response
050-09-07,CTRL - Control,
050-09-08,Security Block,
050-09-09,CMND / REPLY,
050-09-10,Valid command / reply,Command / Reply value in range
050-09-11,CHECKSUM,must support both
050-09-12,SOM Sent,(see old code)
050-09-13,Config address test,
050-09-14,Rogue SCS Poll,
050-10-01,Large Data Arrays,Multi-part message fields added to certain commands and responses

## Test Group 6 – Commands
### Test 3-10-1 LED Test (Red)
### Test 3-10-2 LED Test (Green)
### Test 3-11-1 Buzzer Control
### Test 060-12-01 osdp_COMSET
Test Reference: 060-12-01 (rev.00)
Test Title: osdp_COMSET – set port and speed.
Criteria: (required: basic) supports RS-485 2-wire; cleartext
Test action: issue osdp_COMSET and change ACU speed to match.
Operator action:
confirm acu and pd are communicating (poll/ack counters)
issue osdp_COMSET and also change the test ACU's speed to match
operator monitors statistics to confirm stabilized poll/ack traffc at new speed/address (	confirm at least 8 poll/ack sequences completed.)
issue osdp_ID and capture response
issue osdp_CAP and capture response.

Recommended processing: Note – reset speed and address to 0/9600 before removing DUT from testbed.
Development status: available in current release of libosdp_conformance (0.80-1.)
### Test 060-12-02 osdp_COMSET (SCS)
Test Reference: 060-12-02 (rev.00)
Test Title: osdp_COMSET – set port and speed, within a secure channel session.
Criteria: (required: basic) supports RS-485 2-wire
Test action: within a secure channel session issue osdp_COMSET and change ACU speed to match.
Operator action:
configure for secure channel
execute procedure for 060-12-01.
Recommended processing: Note – reset speed and address to 0/9600 before removing DUT from testbed.
Development status: available in current release of libosdp_conformance (0.80-1.)
### Test 060-16-02 Paired SCS
Test Reference: 060-16-02 (rev 00)
Test Title: Paired SCS
Description: Secure channel session using the paired key not the default key.
Purpose: Exercise use of paired key secure channel sessions.
Criteria: (required: pd-secure) as documented
Test action: configure a secure channel session with the default key, do a keyset to pair, then start the ACU again with a secure channel session on the paired key.
Operator action:
PD test: as documented
ACU test: as documented
Recommended processing: n/a
Development status: Available in libosdp-conformance 0.97-1
Example use: t.b.d.
## Test Group 7 – Responses
### Test 070-02-01 osdp_ACK
Test Reference: 070-02-01 (rev. 01)
Test Title: osdp_ACK response
Description: Default benign response to a poll.
Purpose: PD proof of life.
Criteria: (required: basic) must appear at least once in test sequence.
Test action: capture in trace during automated sequence.
Operator action:
PD test: run test ACU via sequencer, confirm trace analysis shows poll test
ACU test: prepare test PD and run ACU test sequencer.
Recommended processing: use a conventional ACU-PD configuration.
Development status: Available in libosdp-conformance 0.81-1
### Test 070-02-02 OSTATR response to POLL
Test Reference: 070-02-02 (rev. 00)
Test Title: osdp_OSTATR response to a poll
Description:
Purpose:
Criteria: (optional: basic) should work if pdcap reports outputs.
Test action:
Operator action:
PD test:
ACU test:
Recommended processing:
Development status: Available in libosdp-conformance 0.81-2
Example use:
### Test 070-03-01 osdp_NAK
Test Reference: 070-03-01 (rev. 01)
Test Title: osdp_NAK response
Description: Negative acknowledgement with optional reason.
Purpose: Negative feedback..
Criteria: (required: basic) expected at least once due to induced NAK.
Test action: capture in trace during automated sequence.
Operator action:
PD test: run test ACU via sequencer, run nak test
ACU test: prepare test PD and run test to respond with a NAK.
Recommended processing: use a conventional ACU-PD configuration.
Development status: Available in libosdp-conformance 0.81-1
Example use: exceptions reported via the protocol.
### Test 070-03-02 NAK not 1
Test Reference: 070-03-02 (rev. 01)
Test Title: osdp_NAK response (not code 1)
Description: Negative acknowledgement with a cause code other than 1.
Purpose: Exercise NAK mechanism to proove it can provide details.
Criteria: (optional) expected at least once due to induced NAK.
Test action: capture in trace during automated sequence.
Operator action:
PD test: run test ACU via sequencer, run nak test
ACU test: prepare test PD and run test to respond with a NAK.
Recommended processing: use a conventional ACU-PD configuration.
Development status: Available in libosdp-conformance 0.81-1
Example use: NAK with unknown command upon receipt of unimplemented osdp_ACURXSIZE.
### Test 070-04-01 osdp_PDID
Test Reference: 070-04-01 (rev. 01)
Test Title: osdp_PDID response
Description: Confirm PDID response to ID
Purpose:Confirm PD can be identified.
Criteria: (required: basic)
Test action: capture in trace during automated sequence.
Operator action:
PD test: run test ACU via sequencer, send osdp_ID
ACU test: prepare test PD and respoknd with PDID when the ACU test harness induces an ID rquest.
Recommended processing: use a conventional ACU-PD configuration.
Development status: Available in libosdp-conformance 0.81-1
Example use: returns PD identification for ACU set-up.
### Test 070-04-02 Bad PDID
Test Reference: 070-04-02 (rev. 01)
Test Title: osdp_PDID invalid response
Description: Declared if PDID is present but wrong.
Purpose:Confirm PD contains usable and/or documented details.
Criteria: (optional)
Test action: capture in trace during automated sequence.
Operator action:
PD test: run test ACU via sequencer, examine PDID response
ACU test: prepare test PD and respoknd with PDID when the ACU test harness induces an ID request.
Recommended processing: use a conventional ACU-PD configuration.
Development status: Available in libosdp-conformance 0.81-1
Example use: test reflects identified issues in PDID response data.
### Test 070-05-01 osdp_PDCAP
Test Reference: 070-05-01 (rev. 01)
Test Title: osdp_PDCAP response
Description: Confirm PDCAP response to osdp_CAP
Purpose:Confirm PD capabilities can be queried.
Criteria: (required: basic)
Test action: capture in trace during automated sequence; analysis process also checks specific capabilities.
Operator action:
PD test: run test ACU via sequencer, send osdp_CAP
ACU test: prepare test PD and respoknd with PDCAP when the ACU test harness induces an osdp_CAP request.
Recommended processing: use a conventional ACU-PD configuration.
Development status: Available in libosdp-conformance 0.81-1
Example use: retrieve PD capabilities to confirm it supports secure channel.

### Test 070-05-02 Capability: number of inputs
Test Reference: 070-05-02 (rev. 01)
Test Title: Capability - number of inputs
Description: Identify presence of capability no. 1 (number of inputs.)
Purpose:Confirm capability presence and values.
Criteria: (optional: basic)
Test action: capture in trace during automated sequence.
Operator action:
PD test: run test ACU via sequencer, send osdp_CAP, analyze osdp_PDCAP response
ACU test: prepare test PD and respond with PDCAP containing a known value.
Recommended processing: use an ACU-PD configuration that includes I/O signalling.
Development status: Available in libosdp-conformance 0.81-1
Example use: confirm PD has inputs before configuring.
### tbd 070-05-03 through 070-05-xx
070-04-04,capability 2 - number and type of outputs,
070-04-06,capability 4 - number and type of LED,
070-04-07,capability 5 - audible output,
070-04-08,capability 6 - text display,
070-04-11,capability 9 - - report secure channel yes/no,
070-04-15,capability 13 - Number of Readers,
### Test 070-05-17 Capability: OSDP version
Test Reference: 070-05-17 (rev. 00)
Test Title: Capability – OSDP version.
Description: Identify which version of the OSDP protocol this PD implements.
Purpose: Compatibility
Criteria: (recommended: basic)
Test action: capture in trace during automated sequence.
Operator action:
PD test: run test ACU via sequencer, send osdp_CAP, analyze osdp_PDCAP response
ACU test: prepare test PD and respond with PDCAP containing a known value.
Recommended processing: use standard ACU-PD configuration.
Development status: Available in libosdp-conformance 0.81-2
Example use: confirm PD supports SIA 2.2 spec.
### Test 070-06-01 osdp_LSTATR
Test Reference: 070-06-01 (rev. 01)
Test Title: local status report
Description: Reports poweron and tamper state
Purpose: Notify ACU of losso of power or tamper state.
Criteria: (required: basic)
Test action: capture in trace during automated sequence. look for any example including LSTAT response.
Operator action:
PD test: run test ACU via sequencer, send osdp_LSTAT, analyze osdp_LSTATR response
ACU test: prepare test PD and respond with LSTATR simulating power cycle or tamper
Recommended processing: use a conventional ACU-PD configuration.
Development status: Available in libosdp-conformance 0.81-1
Example use: detect PD has gone into Tamper state.
### Test 070-06-02 LSTATR Tamper
Test Reference: 070-06-02 (rev. 00)
Test Title: Local Status Report - Tamper
Description: Reports tamper state
Purpose: Notify ACU of tamper state.
Criteria: (optional: basic)
Test action: capture in trace during automated sequence. look for any example including LSTAT response.
Operator action:
PD test: run test ACU via sequencer, send osdp_LSTAT, analyze osdp_LSTATR response
ACU test: prepare test PD and respond with LSTATR simulating tamper
Recommended processing: use a conventional ACU-PD configuration.
Development status: Available in libosdp-conformance 0.81-1
Example use: detect PD has gone into Tamper state.
### Test 070-06-03 LSTATR Power
Test Reference: 070-05-03 (rev. 00)
Test Title: Local Status Report - Power
Description: Reports power-on state
Purpose: Notify ACU of power cycling.
Criteria: (optional: basic)
Test action: capture in trace during automated sequence. look for any example including LSTAT response.
Operator action:
PD test: run test ACU via sequencer, send osdp_LSTAT, analyze osdp_LSTATR response
ACU test: prepare test PD and respond with LSTATR simulating power restoral.
Recommended processing: use a conventional ACU-PD configuration.
Development status: Available in libosdp-conformance 0.81-1
Example use: detect PD has cycled power.
### Test 070-07-01 osdp_ISTATR
Test Reference: 070-07-01 (rev 00)
Test Title: Input Status Report
Description: reports digital in status
Purpose: Notify ACU of alarm point value changes.
Criteria: optional: basic, required if PDCAP reports inputs.
Test action: Operator-induced I/O signal change.
Operator action:
PD test: query with osdp_ISTAT
ACU test: confirm detection of exerciser-induced input status change.
Recommended processing: Use ACU-PD configuration with 1 digital input and 1 digital output.
Development status: Available in libosdp-conformance 0.80-1
Example use: Alarm points, REX, DFS.
### Test 070-08-01 osdp_OSTATR
Test Reference: 070-08-01 (rev 00)
Test Title: Output Status Report
Description: reports digital out status
Purpose: energize relay.
Criteria: optional: basic, required if PDCAP reports outputs.
Test action: Operator-induced I/O signal change.
Operator action:
PD test: query with osdp_OSTAT
ACU test: confirm exerciser PD detects exerciser-induced output change.
Recommended processing: Use ACU-PD configuration with 1 digital input and 1 digital output.
Development status: Available in libosdp-conformance 0.80-1
Example use: Lock/Unlock.
### Test 070-09-01 osdp_RSTATR
Test Reference: 070-09-01 (rev 00)
Test Title: Reader status report
Description: reports on status of downstream (not the primary) reader
Purpose: control downstream attached readers.
Criteria: (optional: basic)
Test action: checked through automatic sequencer.
Operator action:
PD test: sequencer uses exerciser to request status
ACU test: exerciser reports PD status when queried by ACU
Recommended processing: Use standard ACU/PD with zero downstream readers.
Development status: Available in libosdp-conformance 0.80-1
Example use: (deprecated?)
### Test 070-10-01 osdp_RAW
Test Reference: 070-10-01 (rev 00)
Test Title: Raw card read
Description: reads raw (bits) from credential
Purpose: collect card data.
Criteria: (required: basic)
Test action: Operator controlled.
Operator action:
PD test: operator presents credential, sequencer uses exerciser to record card read.
ACU test: exerciser reports a card read, check it gets through.
Recommended processing: Use standard ACU/PD.
Development status: Available in libosdp-conformance 0.80-1
Example use: card read test
### Test 070-12-01 osdp_KEYPAD
Test Reference: 070-12-01 (rev 00)
Test Title: Keypad
Description: reads keypad input
Purpose: reads keypad
Criteria: optional: basic
Test action: Operator controlled.
Operator action:
PD test: operate keypad and check for input.
ACU test: confirm acu reports induced keypad input.
Recommended processing: Use ACU with a keypad PD.
Development status: Available in libosdp-conformance 0.80-1
Example use: card read test
### Test 070-13-01 osdp_COM
Test Reference: 070-13-01 (rev 00)
Test Title: Communications report
Description: reports new actual speed and address
Purpose: PD configuration
Criteria: (optional: basic)
Test action: Operator controlled.
Operator action:
PD test: operator tests at least 2 speeds.
ACU test: confirm pd exerciser can be configured..
Recommended processing: Use standard ACU/PD.
Development status: Available in libosdp-conformance 0.80-1
Example use: change address from 0 to 1 and back
### tbd 070-14-01 osdp_BIOREADR
00
### tbd 070-15-01 osdp_BIOMATCHR
t.b.d.
### Test 070-16-01 osdp_CCRYPT
Test Reference: 060-16-01 (rev 00)
Test Title: Client Cryptogram response
Description: part of secure channel session set-up sequence
Purpose: return challenge data to ACU to complete session set-up
Criteria: (required: basic)
Test action: activate secure channel and confirm sequence completes properly.
Operator action:
PD test: operator initiates secure channel through exerciser.
ACU test: ACU is induced to establish a secure channel
Recommended processing: Use standard ACU/PD
Development status: Available in libosdp-conformance 0.80-1
Example use: t.b
### Test 070-17-01 osdp_RMAC_I
Test Reference: 070-17-01 (rev 00)
Test Title: Recieve MAC Initialization
Description: return initial rmac value from PD to ACU
Purpose: complete set-up for secure channel.
Criteria: (required: basic)
Test action: activate secure channel and confirm sequence completes properly.
Operator action:
PD test: operator initiates secure channel through exerciser.
ACU test: ACU is induced to establish a secure channel
Recommended processing: Use standard ACU/PD
Development status: Available in libosdp-conformance 0.80-1
Example use: t.b.d.
### Test 070-18-01 osdp_MFGREP
Test Reference: 070-18-01 (rev 00)
Test Title: Manufacturer-specific response
Description:
Purpose:
Criteria: (optional: basic)
Test action:
Operator action:
PD test:
ACU test:
Recommended processing:
Development status:
Example use:

,osdp_FTSTAT,
### 7-18 busy
### 7-19 pivdatar
### 7-20 genauthr
### 7-21 crauthr
### 7-22 mfgstatr
### 7-23 mfgerrr
### 7-24 ftstat
### 7-26 xrd
,osdp_BIOREADR,
,osdp_BIOMATCHR,

## command list 2
060-01-01,osdp_POLL,
060-02-01,osdp_ID,
060-03-01,osdp_CAP,
060-04-01,osdp_LSTAT,
060-05-01,osdp_ISTAT,required unless PDCAP reports 0 inputs
060-06-01,osdp_OSTAT,required unless PDCAP reports 0 outputs
060-07-01,osdp_RSTAT,required unless PDCAP reports 0 readers
060-08-01,osdp_OUT,required unless PDCAP reports 0 outputs
060-09-01,osdp_LED,required if PDCAP reports >0 LED’s
060-10-01,osdp_BUZ,required if PDCAP reports >0 annunicators
060-11-01,osdp_TEXT,required if PDCAP reports >0 displays
060-13-01,osdp_BIOREAD,
060-14-01,osdp_BIOMATCH,
060-15-01,osdp_KEYSET,used by secure channel
060-16-01,osdp_CHLNG,used by secure channel

060-16-02

060-16-03

060-17-01,osdp_SCRYPT,used by secure channel
060-19-01,osdp_ACURXSIZE,
060-25-01,osdp_FILETRANSFER,
060-18-01,osdp_MFG,required if manufacturer has their own special commands.
,osdp_XWR,
,osdp_ABORT,
,osdp_PIVDATA,
,osdp_GENAUTH,
,osdp_CRAUTH,
,osdp_KEEPACTIVE,
### Test 999-99-99 TEMPLATE
Test Reference: 999-99-01 (rev 04)
Test Title: Template
Description:
Purpose:
Criteria: (required: basic) as documented
Test action: as documented
Operator action:
PD test: as documented
ACU test: as documented
Recommended processing: n/a
Development status: Available in libosdp-conformance 0.80-1
Example use: t.b.d.