### Test 050-06-01 Packet Size Limits ACU to PD
The implementation of the standard message set requires all devices to be able to accept packets up to 128 bytes long and be able to tolerate messages addressed to other devices having a total length not exceeding 1440 bytes.

##### If the packet was meant for another device, there should be no adverse condition created in the PD with the limitation. If the PD receives a packet specifically addressed to it which is greater than its reported RX buffer size, it will constitute a protocol error and respond with a NAK code 0x02.

##### PD
PD MUST use multi-byte data encoding when necessary for message processing.
##### ACU
ACU MUST use multi-byte data encoding when necessary for message processing.
#### Purpose
This protocol's primary purpose is to support communication to simple devices on a shared (multi-dropped) channel. This provides a method to process different message sizes in particular large packets (more than 128 bytes, though in general large packets should be avoided.
#### Criteria
Basic OSDP (PD)	Required
Basic OSDP (ACU)	PD Only
Secure Channel (PD)	Required
Secure Channel (ACU)	PD Only
BIO Match (PD)	Required
BIO Match (ACU)	PD Only
BIO Read (PD)	Required
BIO Read (ACU)	PD Only
Extended Packet Mode (PD)	Required
Extended Packet Mode (ACU)	PD Only
Extended Read/Write (PD)	Required
Extended Read/Write (ACU)	PD Only

#### Test action
##### PD Test
Monitor communications to determine proper message processing between the PD and the ACU within the limits determined by the PD capabilities and the package size limits it expresses.
##### ACU Test
Monitor communications to determine proper message processing between the PD and the ACU within the limits determined by the PD capabilities and the package size limits it expresses.
#### Development status
Available in libosdp-conformance 1.31.1-Build-4
#### Test Results
JSON tags
test	050-06-1
test-status	1 for pass, 0 for fail

#### Revision History
New as 2.4.2