OSPD Verified Test Descriptions
1.61-1

# Introduction
How to read this document
about the test naming

uses numbering from published 60839-11-5
# Test Descriptions
## Test Group 5 – Protocol
### Test 050-01-01 Physical Interface
Test Reference: 050-01-01 (rev.01)
Test Title: Physical Interface
Criteria: (required: basic) supports RS-485 2-wire
Test action: plug it in to RS-485 test jig and make sure it works. Requires choosing a speed at which to test.
Operator action:
confirm initial set-up.
confirm interview form complete.
set up at designated address/speed.
connect DUT
confirm at least 8 poll/ack sequences completed.
Recommended processing: n/a
### Test-draft 050-01-02 TCP Interface
t.b.d.
Criteria: (optional) support TCP as implemented in the reference implementation including "kick-not-poll" processing.
Recommended processing: n/a
### Test 050-02-01 Signalling
Test Reference: 050-02-01 (rev. 01)
Test Title: Signalling
Criteria: (required) supports at least one of the designated speeds.
Test action: confirm communications at designated speed. See interview form.
Operator action:
use speed from form
confirm testbed is running at that speed
connect DUT
confirm at least 8 poll/ack sequences completed
Recommended processing: n/a
### Test 050-03-01 Character Encoding
Test Reference: 050-03-01 (rev. 01)
Test Title: Character Encoding
Criteria: (required) support use of all possible 8 bit patterns.
Test action: Use OSDP trace to confirm character coverage.
Operator action:
Exercise DUT through full test set, collecting a trace
Confirm successful operation
Run trace analyzer
Report character coverage
Recommended processing: n/a
### Test 050-04-01 Channel Access
Test Reference: 050-04-01 (rev. 02)
Test Title: Channel Access
Criteria: (required) Confirm only one reply per command; presence of busy; later processing if busy.
Test action: Use OSDP trace to confirm presence of busy, one reply per command.
Operator action:
Set up DUT and run a selection of commands, collecting a trace
Run trace analyzer
Confirm analyzer does not report response anomalies.
Recommended processing: n/a
### Test-draft 050-04-02 Retry
tbd required
at test ACU by command drop a response and send the last command again. make sure the PD behaves correctly - no nak, processes the command again (?)
### Test-draft 050-05-01 Multibyte Encoding
tbd required
?? test from ACU to PD
?? test from PD to ACU
050-05-01,Multi-byte Data Encoding,lsb first unless otherwise noted; no padding.
### Test-draft 050-06-01 Packet Size Limits
tbd required
RUN PDCAP TEST FIRST AND VERIFY PDCAP RESPONSE INCLUDES MAX PACKET SIZE
try a text out at the 128 limit, make sure you get "bad command" not "bad command", then try an out-of-spec packet and make sure you get "bad packet" not "bad command". use pdcap to identify max size claimed to be accepted by PD.

also, send a truly max sized packet using LED commands to a different address and ensure the PD does not fail. fail is defined as reboot, stop accepting poll, etc.
### Test 050-07-01 Timing
Test Reference: 050-07-01 (rev. 00)
Test Title: Timing
Criteria: (required) Confirm command (poll) response time is under 200 milliseconds.
Test action: Use OSDP trace log analyzer to confirm timing.
Operator action:
Set up DUT in idle poll/ack configuration, collecting a trace
Run trace analyzer
Confirm analyzer does not report response time of 200ms exceeded.
Recommended processing: n/a
### Test 050-08-01 Message Synchronization
Test Reference: 050-08-01 (rev. 00)
Test Title: Message Synchronization
Criteria: (required) Passes message traffic (implied.)
Test action: plug it in to RS-485 test jig and make sure it works. Requires choosing a speed at which to test. Assumes proper inter-character timing if the testing works.
Operator action: plug it in.
Recommended processing: n/a; Use a logic analyzer for further verification.
### Test 050-09-01 Packet Format
050-09-01,Packet Format,follow table 1 packet format.
### Other 050 tests
050-02-01,,
050-04-04,,
050-09-16,,
050-01-03,TLS,
050-02-02,"SIgnalling 19,200",
050-02-03,"Signalling 38,400",
050-02-04,"Signalling 115,200",
050-02-05,"Signalling 57,600",
050-02-06,"Signalling 230,400",
050-04-03,resend busy,
050-04-04,new after busy,

050-06-01,Packet Size Limits ACU to PD,accept at least 128 bytes total pdu size; accept max 1440 bytes total PDU size.
050-06-02,Packet Size Limits PD to ACU,

050-09-02,,process sequence 0
050-09-03,SOM - Start of Message,SOM starts each OSDP command and response
050-09-04,ADDR - Address,Address field indicates PD address 0x00-0x7e inclusive or special configuration address 0x7f
050-09-05,,"must not use 7f except for ID,PDID, CAP, PDCAP, COM, COMSET"
050-09-06,LEN - Length,Length field (2 bytes LSB MSB) indicates length of OSDP command and response
050-09-07,CTRL - Control,
050-09-08,Security Block,
050-09-09,CMND / REPLY,
050-09-10,Valid command / reply,Command / Reply value in range
050-09-11,CHECKSUM,must support both
050-09-12,SOM Sent,(see old code)
050-09-13,Config address test,
050-09-14,Rogue SCS Poll,
050-09-15,CRC,
050-10-01,Large Data Arrays,Multi-part message fields added to certain commands and responses

## Test Group 6 – Commands
### Test 3-10-1 LED Test (Red)
### Test 3-10-2 LED Test (Green)
### Test 3-11-1 Buzzer Control
### Test 060-12-01 osdp_COMSET
Test Reference: 060-12-01 (rev.00)
Test Title: osdp_COMSET – set port and speed.
Criteria: (required: basic) supports RS-485 2-wire; cleartext
Test action: issue osdp_COMSET and change ACU speed to match.
Operator action:
confirm acu and pd are communicating (poll/ack counters)
issue osdp_COMSET and also change the test ACU's speed to match
operator monitors statistics to confirm stabilized poll/ack traffc at new speed/address (	confirm at least 8 poll/ack sequences completed.)
issue osdp_ID and capture response
issue osdp_CAP and capture response.

Recommended processing: Note – reset speed and address to 0/9600 before removing DUT from testbed.
Development status: available in current release of libosdp_conformance (0.80-1.)
### Test 060-12-02 osdp_COMSET (SCS)
Test Reference: 060-12-02 (rev.00)
Test Title: osdp_COMSET – set port and speed, within a secure channel session.
Criteria: (required: basic) supports RS-485 2-wire
Test action: within a secure channel session issue osdp_COMSET and change ACU speed to match.
Operator action:
configure for secure channel
execute procedure for 060-12-01.
Recommended processing: Note – reset speed and address to 0/9600 before removing DUT from testbed.
Development status: available in current release of libosdp_conformance (0.80-1.)
### Test 060-16-02 Paired SCS
Test Reference: 060-16-02 (rev 00)
Test Title: Paired SCS
Description: Secure channel session using the paired key not the default key.
Purpose: Exercise use of paired key secure channel sessions.
Criteria: (required: pd-secure) as documented
Test action: configure a secure channel session with the default key, do a keyset to pair, then start the ACU again with a secure channel session on the paired key.
Operator action:
PD test: as documented
ACU test: as documented
Recommended processing: n/a
Development status: Available in libosdp-conformance 0.97-1
Example use: t.b.d.
## Test Group 7 – Responses
### Test 070-02-01 osdp_ACK
Test Reference: 070-02-01 (rev. 01)
Test Title: osdp_ACK response
Description: Default benign response to a poll.
Purpose: PD proof of life.
Criteria: (required: basic) must appear at least once in test sequence.
Test action: capture in trace during automated sequence.
Operator action:
PD test: run test ACU via sequencer, confirm trace analysis shows poll test
ACU test: prepare test PD and run ACU test sequencer.
Recommended processing: use a conventional ACU-PD configuration.
Development status: Available in libosdp-conformance 0.81-1
### Test 070-02-02 OSTATR response to POLL
Test Reference: 070-02-02 (rev. 00)
Test Title: osdp_OSTATR response to a poll
Description:
Purpose:
Criteria: (optional: basic) should work if pdcap reports outputs.
Test action:
Operator action:
PD test:
ACU test:
Recommended processing:
Development status: Available in libosdp-conformance 0.81-2
Example use:
### Test 070-03-01 osdp_NAK
Test Reference: 070-03-01 (rev. 01)
Test Title: osdp_NAK response
Description: Negative acknowledgement with optional reason.
Purpose: Negative feedback..
Criteria: (required: basic) expected at least once due to induced NAK.
Test action: capture in trace during automated sequence.
Operator action:
PD test: run test ACU via sequencer, run nak test
ACU test: prepare test PD and run test to respond with a NAK.
Recommended processing: use a conventional ACU-PD configuration.
Development status: Available in libosdp-conformance 0.81-1
Example use: exceptions reported via the protocol.
### Test 070-03-02 NAK not 1
Test Reference: 070-03-02 (rev. 01)
Test Title: osdp_NAK response (not code 1)
Description: Negative acknowledgement with a cause code other than 1.
Purpose: Exercise NAK mechanism to proove it can provide details.
Criteria: (optional) expected at least once due to induced NAK.
Test action: capture in trace during automated sequence.
Operator action:
PD test: run test ACU via sequencer, run nak test
ACU test: prepare test PD and run test to respond with a NAK.
Recommended processing: use a conventional ACU-PD configuration.
Development status: Available in libosdp-conformance 0.81-1
Example use: NAK with unknown command upon receipt of unimplemented osdp_ACURXSIZE.
### Test 070-04-01 osdp_PDID
Test Reference: 070-04-01 (rev. 01)
Test Title: osdp_PDID response
Description: Confirm PDID response to ID
Purpose:Confirm PD can be identified.
Criteria: (required: basic)
Test action: capture in trace during automated sequence.
Operator action:
PD test: run test ACU via sequencer, send osdp_ID
ACU test: prepare test PD and respoknd with PDID when the ACU test harness induces an ID rquest.
Recommended processing: use a conventional ACU-PD configuration.
Development status: Available in libosdp-conformance 0.81-1
Example use: returns PD identification for ACU set-up.
### Test 070-04-02 Bad PDID
Test Reference: 070-04-02 (rev. 01)
Test Title: osdp_PDID invalid response
Description: Declared if PDID is present but wrong.
Purpose:Confirm PD contains usable and/or documented details.
Criteria: (optional)
Test action: capture in trace during automated sequence.
Operator action:
PD test: run test ACU via sequencer, examine PDID response
ACU test: prepare test PD and respoknd with PDID when the ACU test harness induces an ID request.
Recommended processing: use a conventional ACU-PD configuration.
Development status: Available in libosdp-conformance 0.81-1
Example use: test reflects identified issues in PDID response data.
### Test 070-05-01 osdp_PDCAP
Test Reference: 070-05-01 (rev. 01)
Test Title: osdp_PDCAP response
Description: Confirm PDCAP response to osdp_CAP
Purpose:Confirm PD capabilities can be queried.
Criteria: (required: basic)
Test action: capture in trace during automated sequence; analysis process also checks specific capabilities.
Operator action:
PD test: run test ACU via sequencer, send osdp_CAP
ACU test: prepare test PD and respoknd with PDCAP when the ACU test harness induces an osdp_CAP request.
Recommended processing: use a conventional ACU-PD configuration.
Development status: Available in libosdp-conformance 0.81-1
Example use: retrieve PD capabilities to confirm it supports secure channel.

### Test 070-05-02 Capability: number of inputs
Test Reference: 070-05-02 (rev. 01)
Test Title: Capability - number of inputs
Description: Identify presence of capability no. 1 (number of inputs.)
Purpose:Confirm capability presence and values.
Criteria: (optional: basic)
Test action: capture in trace during automated sequence.
Operator action:
PD test: run test ACU via sequencer, send osdp_CAP, analyze osdp_PDCAP response
ACU test: prepare test PD and respond with PDCAP containing a known value.
Recommended processing: use an ACU-PD configuration that includes I/O signalling.
Development status: Available in libosdp-conformance 0.81-1
Example use: confirm PD has inputs before configuring.
### tbd 070-05-03 through 070-05-xx
070-04-04,capability 2 - number and type of outputs,
070-04-06,capability 4 - number and type of LED,
070-04-07,capability 5 - audible output,
070-04-08,capability 6 - text display,
070-04-11,capability 9 - - report secure channel yes/no,
070-04-15,capability 13 - Number of Readers,
### Test 070-05-17 Capability: OSDP version
Test Reference: 070-05-17 (rev. 00)
Test Title: Capability – OSDP version.
Description: Identify which version of the OSDP protocol this PD implements.
Purpose: Compatibility
Criteria: (recommended: basic)
Test action: capture in trace during automated sequence.
Operator action:
PD test: run test ACU via sequencer, send osdp_CAP, analyze osdp_PDCAP response
ACU test: prepare test PD and respond with PDCAP containing a known value.
Recommended processing: use standard ACU-PD configuration.
Development status: Available in libosdp-conformance 0.81-2
Example use: confirm PD supports SIA 2.2 spec.
### Test 070-06-01 osdp_LSTATR
Test Reference: 070-06-01 (rev. 01)
Test Title: local status report
Description: Reports poweron and tamper state
Purpose: Notify ACU of losso of power or tamper state.
Criteria: (required: basic)
Test action: capture in trace during automated sequence. look for any example including LSTAT response.
Operator action:
PD test: run test ACU via sequencer, send osdp_LSTAT, analyze osdp_LSTATR response
ACU test: prepare test PD and respond with LSTATR simulating power cycle or tamper
Recommended processing: use a conventional ACU-PD configuration.
Development status: Available in libosdp-conformance 0.81-1
Example use: detect PD has gone into Tamper state.
### Test 070-06-02 LSTATR Tamper
Test Reference: 070-06-02 (rev. 00)
Test Title: Local Status Report - Tamper
Description: Reports tamper state
Purpose: Notify ACU of tamper state.
Criteria: (optional: basic)
Test action: capture in trace during automated sequence. look for any example including LSTAT response.
Operator action:
PD test: run test ACU via sequencer, send osdp_LSTAT, analyze osdp_LSTATR response
ACU test: prepare test PD and respond with LSTATR simulating tamper
Recommended processing: use a conventional ACU-PD configuration.
Development status: Available in libosdp-conformance 0.81-1
Example use: detect PD has gone into Tamper state.
### Test 070-06-03 LSTATR Power
Test Reference: 070-05-03 (rev. 00)
Test Title: Local Status Report - Power
Description: Reports power-on state
Purpose: Notify ACU of power cycling.
Criteria: (optional: basic)
Test action: capture in trace during automated sequence. look for any example including LSTAT response.
Operator action:
PD test: run test ACU via sequencer, send osdp_LSTAT, analyze osdp_LSTATR response
ACU test: prepare test PD and respond with LSTATR simulating power restoral.
Recommended processing: use a conventional ACU-PD configuration.
Development status: Available in libosdp-conformance 0.81-1
Example use: detect PD has cycled power.
### Test 070-07-01 osdp_ISTATR
Test Reference: 070-07-01 (rev 00)
Test Title: Input Status Report
Description: reports digital in status
Purpose: Notify ACU of alarm point value changes.
Criteria: optional: basic, required if PDCAP reports inputs.
Test action: Operator-induced I/O signal change.
Operator action:
PD test: query with osdp_ISTAT
ACU test: confirm detection of exerciser-induced input status change.
Recommended processing: Use ACU-PD configuration with 1 digital input and 1 digital output.
Development status: Available in libosdp-conformance 0.80-1
Example use: Alarm points, REX, DFS.
### Test 070-08-01 osdp_OSTATR
Test Reference: 070-08-01 (rev 00)
Test Title: Output Status Report
Description: reports digital out status
Purpose: energize relay.
Criteria: optional: basic, required if PDCAP reports outputs.
Test action: Operator-induced I/O signal change.
Operator action:
PD test: query with osdp_OSTAT
ACU test: confirm exerciser PD detects exerciser-induced output change.
Recommended processing: Use ACU-PD configuration with 1 digital input and 1 digital output.
Development status: Available in libosdp-conformance 0.80-1
Example use: Lock/Unlock.
### Test 070-09-01 osdp_RSTATR
Test Reference: 070-09-01 (rev 00)
Test Title: Reader status report
Description: reports on status of downstream (not the primary) reader
Purpose: control downstream attached readers.
Criteria: (optional: basic)
Test action: checked through automatic sequencer.
Operator action:
PD test: sequencer uses exerciser to request status
ACU test: exerciser reports PD status when queried by ACU
Recommended processing: Use standard ACU/PD with zero downstream readers.
Development status: Available in libosdp-conformance 0.80-1
Example use: (deprecated?)
### Test 070-10-01 osdp_RAW
Test Reference: 070-10-01 (rev 00)
Test Title: Raw card read
Description: reads raw (bits) from credential
Purpose: collect card data.
Criteria: (required: basic)
Test action: Operator controlled.
Operator action:
PD test: operator presents credential, sequencer uses exerciser to record card read.
ACU test: exerciser reports a card read, check it gets through.
Recommended processing: Use standard ACU/PD.
Development status: Available in libosdp-conformance 0.80-1
Example use: card read test
### Test 070-12-01 osdp_KEYPAD
Test Reference: 070-12-01 (rev 00)
Test Title: Keypad
Description: reads keypad input
Purpose: reads keypad
Criteria: optional: basic
Test action: Operator controlled.
Operator action:
PD test: operate keypad and check for input.
ACU test: confirm acu reports induced keypad input.
Recommended processing: Use ACU with a keypad PD.
Development status: Available in libosdp-conformance 0.80-1
Example use: card read test
### Test 070-13-01 osdp_COM
Test Reference: 070-13-01 (rev 00)
Test Title: Communications report
Description: reports new actual speed and address
Purpose: PD configuration
Criteria: (optional: basic)
Test action: Operator controlled.
Operator action:
PD test: operator tests at least 2 speeds.
ACU test: confirm pd exerciser can be configured..
Recommended processing: Use standard ACU/PD.
Development status: Available in libosdp-conformance 0.80-1
Example use: change address from 0 to 1 and back
### tbd 070-14-01 osdp_BIOREADR
00
### tbd 070-15-01 osdp_BIOMATCHR
t.b.d.
### Test 070-16-01 osdp_CCRYPT
Test Reference: 060-16-01 (rev 00)
Test Title: Client Cryptogram response
Description: part of secure channel session set-up sequence
Purpose: return challenge data to ACU to complete session set-up
Criteria: (required: basic)
Test action: activate secure channel and confirm sequence completes properly.
Operator action:
PD test: operator initiates secure channel through exerciser.
ACU test: ACU is induced to establish a secure channel
Recommended processing: Use standard ACU/PD
Development status: Available in libosdp-conformance 0.80-1
Example use: t.b
### Test 070-17-01 osdp_RMAC_I
Test Reference: 070-17-01 (rev 00)
Test Title: Recieve MAC Initialization
Description: return initial rmac value from PD to ACU
Purpose: complete set-up for secure channel.
Criteria: (required: basic)
Test action: activate secure channel and confirm sequence completes properly.
Operator action:
PD test: operator initiates secure channel through exerciser.
ACU test: ACU is induced to establish a secure channel
Recommended processing: Use standard ACU/PD
Development status: Available in libosdp-conformance 0.80-1
Example use: t.b.d.
### Test 070-18-01 osdp_MFGREP
Test Reference: 070-18-01 (rev 00)
Test Title: Manufacturer-specific response
Description:
Purpose:
Criteria: (optional: basic)
Test action:
Operator action:
PD test:
ACU test:
Recommended processing:
Development status:
Example use:

,osdp_FTSTAT,
### 7-18 busy
### 7-19 pivdatar
### 7-20 genauthr
### 7-21 crauthr
### 7-22 mfgstatr
### 7-23 mfgerrr
### 7-24 ftstat
### 7-26 xrd
,osdp_BIOREADR,
,osdp_BIOMATCHR,

## command list 2
060-01-01,osdp_POLL,
060-02-01,osdp_ID,
060-03-01,osdp_CAP,
060-04-01,osdp_LSTAT,
060-05-01,osdp_ISTAT,required unless PDCAP reports 0 inputs
060-06-01,osdp_OSTAT,required unless PDCAP reports 0 outputs
060-07-01,osdp_RSTAT,required unless PDCAP reports 0 readers
060-08-01,osdp_OUT,required unless PDCAP reports 0 outputs
060-09-01,osdp_LED,required if PDCAP reports >0 LED’s
060-10-01,osdp_BUZ,required if PDCAP reports >0 annunicators
060-11-01,osdp_TEXT,required if PDCAP reports >0 displays
060-13-01,osdp_BIOREAD,
060-14-01,osdp_BIOMATCH,
060-15-01,osdp_KEYSET,used by secure channel
060-16-01,osdp_CHLNG,used by secure channel

060-16-02

060-16-03

060-17-01,osdp_SCRYPT,used by secure channel
060-19-01,osdp_ACURXSIZE,
060-25-01,osdp_FILETRANSFER,
060-18-01,osdp_MFG,required if manufacturer has their own special commands.
,osdp_XWR,
,osdp_ABORT,
,osdp_PIVDATA,
,osdp_GENAUTH,
,osdp_CRAUTH,
,osdp_KEEPACTIVE,
### Test 999-99-99 TEMPLATE
Test Reference: 999-99-01 (rev 04)
Test Title: Template
Description:
Purpose:
Criteria: (required: basic) as documented
Test action: as documented
Operator action:
PD test: as documented
ACU test: as documented
Recommended processing: n/a
Development status: Available in libosdp-conformance 0.80-1
Example use: t.b.d.